## Slide 1
MORGAN STATE UNIVERSITY / MSU-2
Task 2: SPI performance,
determinism and secure integration
Evidence review: completed comparisons, simulation findings, and remaining verification work
ZCU102 · AXI Quad SPI · J55 loopback · Evidence through 15 October 2026
Notes: Scope: Task 2a–2c findings and current status of remaining SOW activities.
Primary source: /home/opentitan/Downloads/MSU-2_SOW_Final (1).docx, revision 2026-02-23.

## Slide 2
2A / PERFORMANCE GAP
Linux and bare metal cross over by payload size
MSU-2 · Task 2 evidence review · 15 Oct 2026 02
Chart: Payload size
| 1 B | 8 B | 16 B | 64 B | 128 B | 256 B | 512 B | 1,024 B | 4,096 B | 16,384 B | 65,536 B
Bare metal | 0.14447 | 0.47299 | 0.56501 | 0.65997 | 0.67907 | 0.68904 | 0.87526 | 1.0155 | 1.1543 | 1.1951 | 1.2058
Linux | 0.035675 | 0.26339 | 0.47772 | 0.99107 | 1.2038 | 1.3499 | 1.4265 | 1.4683 | 1.5023 | 1.5115 | 1.514
11,000 transfers per path
Zero API errors and zero RX mismatches in both captured runs.
Crossover: 16–64 bytes
Linux is slower for 1–16 B and faster from 64 B upward in this run. Rates include end-to-end software cost; they are not wire throughput.
Measured paths: SPI ioctl vs XSpi interrupt transfer.
Notes: Source: results/linux_axi_spi_bringup_20261013/linux_vs_baremetal_comparison_20261014.csv.
Method and limitations: results/linux_axi_spi_bringup_20261013/SOW_2A_FINAL_COMPARISON_20261014.md.
Both paths used the same AXI Quad SPI hardware, J55 external loopback, payload vectors and 1,000 trials per size. Linux used CLOCK_MONOTONIC_RAW; bare metal used XTime_GetTime. No timer cross-calibration was recorded.

## Slide 3
2B / PIO AND DMA MECHANISMS
CDMA loopback simulation passes six payload sizes
MSU-2 · Task 2 evidence review · 15 Oct 2026 03
Chart: Payload size
| 1 B | 8 B | 16 B | 64 B | 128 B | 256 B
Simulated effective rate | 0.34602 | 0.68847 | 0.73529 | 0.76757 | 0.77548 | 0.77835
2b assessment complete
6 / 6 simulated DMA sizes passed; every received byte matched.
What this proves
The AXI CDMA keyhole path can feed the modeled AXI Quad SPI DTR and complete internal-loopback transfers.
PIO is physically measured on slide 2. DMA points here are simulation only; no physical DMA or crossover is claimed.
Notes: Source: results/task2b_cdma_sim_20261014/cdma_simulated_sweep.csv and results/task2b_cdma_sim_20261014/cdma_loopback_simulate.log.
Reproduction and test limits: results/task2b_cdma_sim_20261014/README.md; source testbench: hardware/sim/tb_keyhole.sv.
Optional physical follow-on experiment design and readiness gate: results/SOW_2B_PHYSICAL_DMA_EXPERIMENT_DESIGN_20261015.md. No CDMA-enabled bitstream is currently in the repository.
Vivado 2025.1 fresh build and XSim run passed with host IPC access. The chart shows model effective rate from the BTT write to TX FIFO empty plus the stated 2 us final-word allowance.

## Slide 4
2C / REAL-TIME SUITABILITY
Linux timing spread grows as CPU frequency falls
MSU-2 · Task 2 evidence review · 15 Oct 2026 04
Chart: A53 CPU operating point
| 1,200 MHz | 600 MHz | 400 MHz | 300 MHz
64 KiB standard deviation | 3.87 | 5.17 | 8.65 | 14.23
2c assessment complete
44,000 frequency-sweep transfers; zero reported errors.
At 64 KiB, standard deviation rises 3.7× from 1,200 to 300 MHz.
Observed timing is variable and frequency-sensitive. These captures do not define a deadline or establish hard real-time behavior; they do not identify the cause of the spread.
Notes: Frequency sweep source: results/SOW_2F_FREQSWEEP_20260908.md; raw capture: docs/environment/zcu102-2_2f_freqsweep_20260908.log.
Cross-OS timing source: results/linux_axi_spi_bringup_20261013/SOW_2A_FINAL_COMPARISON_20261014.md.
The 64 KiB standard deviations are 3.87, 5.17, 8.65 and 14.23 us at 1,200, 600, 400 and 300 MHz. The frequency-sweep report records zero errors and ivcsw=0; those results do not attribute a jitter mechanism.

## Slide 5
STATUS / 14 OCTOBER 2026
Remaining Task 2 work and evidence boundary
MSU-2 · Task 2 evidence review · 15 Oct 2026 05
2d System hardening
Design complete
Verified boot and signed update implementation remain open.
2e Benchmark framework
Partial
Paired contract and CPU analysis exist; bare-metal CPU measurement and sustained-throughput test remain open.
2f OS tuning
Partial
CPU-frequency axis measured; preemption-model and physical DMA driver comparisons remain open.
2g Minimal appliance
Partial
A/B updater prototype passes host fault tests; U-Boot integration and target secure boot/recovery remain open.
Status labels follow the SOW activity wording; partial evidence is not presented as criterion closure.
Notes: SOW source: /home/opentitan/Downloads/MSU-2_SOW_Final (1).docx, revision 2026-02-23.
2d/2e audit basis: results/SOW_2E_HARDENED_BOARD_VALIDATION_20260922.md and results/linux_axi_spi_bringup_20261013/SOW_2A_FINAL_COMPARISON_20261014.md.
2f source: results/SOW_2F_FREQSWEEP_20260908.md. 2g sources: results/SOW_2G_RECOVERY_20260909.md and results/SOW_2G_FWENV_20260908.md.
Historical file labels do not exactly mirror the SOW’s unlettered activity list. This slide maps 2d–2g by the SOW’s wording and sequence.

## Slide 6
2D / SYSTEM HARDENING DESIGN
Proposed boot trust and rollback architecture
MSU-2 · Task 2 evidence review · 15 Oct 2026 06
BOOT AUTHENTICATION
2d DESIGN CRITERION COMPLETE
Immutable key
Approved PPK hash
held by device
BootROM + FSBL
Authenticate first-stage
boot code
BOOT.BIN
Verify PMUFW, PL,
ATF and U-Boot
Signed FIT
Verify kernel, DTB
and root filesystem
Read-only OS
Run only the
authenticated release
UPDATE TRANSACTION AND AUTOMATIC ROLLBACK
Stage inactive slot
Keep confirmed
slot untouched
Verify release
Check signature,
digest and image
Trial boot
Bounded attempt
count and logs
Health check
Linux start + SPI
loopback smoke test
Confirm / rollback
Mark good or return
to prior slot
Design only: no signed boot image or A/B update is deployed. Development boot-header authentication is not fielded eFUSE-rooted trust. No eFUSE was programmed.
Notes: Design source: results/SOW_2D_SYSTEM_HARDENING_DESIGN_20261014.md.
Existing U-Boot environment fallback evidence and limitations: results/SOW_2G_RECOVERY_20260909.md.
AMD Zynq UltraScale+ MPSoC Software Developer Guide, Boot Time Security: https://docs.amd.com/r/en-US/ug1137-zynq-ultrascale-mpsoc-swdev/Boot-Time-Security.
AMD Embedded Design Tutorial, Enabling Boot Header Authentication: https://docs.amd.com/r/en-US/ug1209-embedded-design-tutorial/Enabling-Boot-Header-Authentication. Boot-header authentication omits the eFUSE key-hash and revocation checks; it is a development mechanism, not the fielded trust anchor.

## Slide 7
2E / COMPARATIVE FRAMEWORK STATUS
Linux thread CPU share declines as payload grows
MSU-2 · Task 2 evidence review · 15 Oct 2026 07
Chart: Payload size
| 1 B | 8 B | 16 B | 64 B | 128 B | 256 B | 512 B | 1,024 B | 4,096 B | 16,384 B | 65,536 B
Linux benchmark thread | 67.876 | 68.199 | 66.691 | 46.809 | 38.577 | 32.88 | 18.051 | 10.002 | 3.577 | 1.912 | 1.474
11,000 paired transfers
Zero transfer errors and RX mismatches in both recorded runs.
Linux thread CPU share: 67.9% at 1 B → 1.5% at 64 KiB.
Scope: benchmark thread over the 1,000-transfer loop. Bare-metal CPU use was not instrumented, and this fixed ladder does not establish maximum sustainable throughput.
Notes: Source CSV: results/linux_axi_spi_bringup_20261013/task2e_framework_metrics_20261014.csv.
Derived from raw Linux CLOCK_THREAD_CPUTIME_ID and CLOCK_MONOTONIC_RAW loop totals in results/linux_axi_spi_bringup_20261013/linux_benchmark_20261014.log.
Framework status and scope: results/SOW_2E_BENCHMARK_FRAMEWORK_STATUS_20261014.md. The utilization percentage is per benchmark thread normalized to one CPU core, not total system CPU utilization.
Physical closure experiment and remaining metric definitions: results/SOW_2E_BENCHMARK_CLOSURE_EXPERIMENT_20261015.md.

## Slide 8
2G / MINIMAL STACK AND ROBUST UPDATE
A/B update prototype preserves the confirmed slot
MSU-2 · Task 2 evidence review · 15 Oct 2026 08
Authenticate
RSA/SHA-256
signature
Write inactive
Chunked write
+ fsync
Readback check
Digest + signature
re-verified
Trial boot
Two bounded
attempts
Confirm / rollback
Health result selects
new or known-good
4 / 4 HOST FAULT-INJECTION TESTS PASSED
Confirmed slot A stayed selected after invalid signatures, interrupted writes, boot-limit expiry, and an explicit failed health check.
Prototype boundary: host files and JSON control state. No U-Boot, SD-card, signed target image, hardware trust anchor, or ZCU102 power-loss test.
Task 2g remains partial until target integration, boot authentication, and recovery fault tests pass.
Notes: Report: results/SOW_2G_AB_UPDATE_PROTOTYPE_20261014.md.
Prototype: linux/appliance/ab_update_prototype.py. Tests: tests/test_task2g_ab_update.py.
Existing on-target U-Boot environment fallback evidence: results/SOW_2G_RECOVERY_20260909.md; it is a single-copy CRC fallback, not image/rootfs update recovery.
All four host tests passed on 2026-10-14. The diagram depicts reference logic, not an installed or hardware-rooted boot chain.

## Slide 9
TOOLCHAIN / LICENSE DIAGNOSTIC
Enterprise license passes ZCU9EG synthesis
MSU-2 · Task 2 evidence review · 15 Oct 2026 09
Sandboxed check
FlexNet could not read the workstation network-interface ID. It reported the node-locked license as invalid; Vivado then surfaced the failed checkout as an expired Synthesis feature.
Normal host access
The permanent Enterprise license matched the active workstation NIC. FlexNet approved the node, and Vivado granted Synthesis for xczu9eg.
Fresh synthesis for xczu9eg-ffvb1156-2-e completed with 0 errors
This was a small license-check design, not the project build. Synthesis uses the selected FPGA part; it does not communicate with the physical ZCU102 board.
Notes: Diagnostic report: results/vivado_license_diagnostic_20261015/README.md.
Successful Vivado 2025.1 synthesis transcript: results/vivado_license_diagnostic_20261015/zcu9eg_license_synthesis.log.
AMD Vivado 2025.1 UG973, Supported Devices: https://docs.amd.com/r/2025.1-English/ug973-vivado-release-notes-install-license/Supported-Devices. The Enterprise edition supports all Zynq UltraScale+ MPSoC devices.