## Slide 1
MORGAN STATE UNIVERSITY / MSU-2
Task 2: SPI performance,
determinism and secure integration
Evidence review: completed comparisons, simulation findings, and remaining verification work
ZCU102 · AXI Quad SPI · J55 loopback · Evidence through 17 October 2026
Notes: Scope: Task 2a–2c findings and current status of remaining SOW activities.
Primary source: /home/opentitan/Downloads/MSU-2_SOW_Final (1).docx, revision 2026-02-23.

## Slide 2
2A / PERFORMANCE GAP
Linux and bare metal cross over by payload size
MSU-2 · Task 2 evidence review · 17 Oct 2026 02
Chart: Payload size
| 1 B | 8 B | 16 B | 64 B | 128 B | 256 B | 512 B | 1,024 B | 4,096 B | 16,384 B | 65,536 B
Bare metal | 0.14447 | 0.47299 | 0.56501 | 0.65997 | 0.67907 | 0.68904 | 0.87526 | 1.0155 | 1.1543 | 1.1951 | 1.2058
Linux | 0.035675 | 0.26339 | 0.47772 | 0.99107 | 1.2038 | 1.3499 | 1.4265 | 1.4683 | 1.5023 | 1.5115 | 1.514
11,000 transfers per path
Zero API errors and zero RX mismatches in both captured runs.
Crossover: 16–64 bytes
Linux is slower for 1–16 B and faster from 64 B upward in this run. Rates include end-to-end software cost; they are not wire throughput.
Measured paths: SPI ioctl vs XSpi interrupt transfer.
Notes: Source: results/linux_axi_spi_bringup_20261013/linux_vs_baremetal_comparison_20261014.csv.
Method and limitations: results/linux_axi_spi_bringup_20261013/SOW_2A_FINAL_COMPARISON_20261014.md.
Both paths used the same AXI Quad SPI hardware, J55 external loopback, payload vectors and 1,000 trials per size. Linux used CLOCK_MONOTONIC_RAW; bare metal used XTime_GetTime. No timer cross-calibration was recorded.

## Slide 3
2B / PIO AND DMA MECHANISMS
CDMA loopback simulation passes six payload sizes
MSU-2 · Task 2 evidence review · 17 Oct 2026 03
Chart: Payload size
| 1 B | 8 B | 16 B | 64 B | 128 B | 256 B
Simulated effective rate | 0.34602 | 0.68847 | 0.73529 | 0.76757 | 0.77548 | 0.77835
2b assessment complete
6 / 6 simulated DMA sizes passed; every received byte matched.
What this proves
The AXI CDMA keyhole path can feed the modeled AXI Quad SPI DTR and complete internal-loopback transfers.
PIO is physically measured on slide 2. DMA points here are simulation only; no physical DMA or crossover is claimed.
Notes: Source: results/task2b_cdma_sim_20261014/cdma_simulated_sweep.csv and results/task2b_cdma_sim_20261014/cdma_loopback_simulate.log.
Reproduction and test limits: results/task2b_cdma_sim_20261014/README.md; source testbench: hardware/sim/tb_keyhole.sv.
Optional physical follow-on experiment design and readiness gate: results/SOW_2B_PHYSICAL_DMA_EXPERIMENT_DESIGN_20261015.md. No CDMA-enabled bitstream is currently in the repository.
Vivado 2025.1 fresh build and XSim run passed with host IPC access. The chart shows model effective rate from the BTT write to TX FIFO empty plus the stated 2 us final-word allowance.

## Slide 4
2C / REAL-TIME SUITABILITY
Linux timing spread grows as CPU frequency falls
MSU-2 · Task 2 evidence review · 17 Oct 2026 04
Chart: A53 CPU operating point
| 1,200 MHz | 600 MHz | 400 MHz | 300 MHz
64 KiB standard deviation | 3.87 | 5.17 | 8.65 | 14.23
2c assessment complete
44,000 frequency-sweep transfers; zero reported errors.
At 64 KiB, standard deviation rises 3.7× from 1,200 to 300 MHz.
Observed timing is variable and frequency-sensitive. These captures do not define a deadline or establish hard real-time behavior; they do not identify the cause of the spread.
Notes: Frequency sweep source: results/SOW_2F_FREQSWEEP_20260908.md; raw capture: docs/environment/zcu102-2_2f_freqsweep_20260908.log.
Cross-OS timing source: results/linux_axi_spi_bringup_20261013/SOW_2A_FINAL_COMPARISON_20261014.md.
The 64 KiB standard deviations are 3.87, 5.17, 8.65 and 14.23 us at 1,200, 600, 400 and 300 MHz. The frequency-sweep report records zero errors and ivcsw=0; those results do not attribute a jitter mechanism.

## Slide 5
STATUS / 17 OCTOBER 2026
Task 2 status against the SOW activity list
MSU-2 · Task 2 evidence review · 17 Oct 2026 05
2a Performance gaps
Complete
Revalidated 11 sizes × 1,000 on both paths; zero errors. Bounded comparison, not causal kernel-only attribution.
2b PIO and DMA
Assessment complete
Physical PIO; six-size CDMA simulation; ZDMA result invalid for performance. No physical DMA crossover.
2c Real-time suitability
Assessment complete
Best-effort latency and jitter characterized; no hard deadline or deterministic guarantee established.
2d System hardening
Design complete
Design documented. Verified boot, reliable updates and automatic recovery are not deployed.
2e Benchmark framework
Partial
66/66 paired sustained points pass. Reliable clock/payload stress envelope remains to be measured before 2e closes.
2f OS tuning
Partial
CPU-frequency sweep done; preemption-model and physical optimized-DMA comparison remain open.
2g Minimal appliance/security
Partial
Prototypes pass defined tests; active boot is unsigned and integrated target recovery remains open.
SOW wording is authoritative; 2a–2g are internal labels. Task 1 and formal reporting deliverables are assessed separately.
Notes: Governing source: /home/opentitan/Downloads/MSU-2_SOW_Final (1).docx, revision 2026-02-23. The seven activity names are quoted or closely abbreviated from Task 2; internal labels 2a–2g are mapped in sequence.
Evidence basis: results/MSU2_TASK2_SOW_STATUS_20261016.md and the source reports in results/ for Task 2a–2g.
Task 2a has a fixed-workload comparison revalidated on 16 October, but timer sources and CPU-point differences limit causal attribution. Task 2b has simulation but no valid physical DMA sweep. Task 2c supports best-effort suitability only. Task 2d is design-only. Task 2e has a complete fixed-trial comparison and 33/33 sustained points per backend, with CPU-metric bases and clock readback documented. Task 2e remains partial because the reliable clock/payload stress envelope has not yet been measured. Task 2f lacks a changed preemption configuration and valid physical optimized-DMA comparison. Task 2g lacks integrated target verified boot and persistent recovery.
The SOW also requires separate Task 1 work and formal monthly, interim, simulation/emulation, OS/appliance, and final-report deliverables; this Task 2 status slide does not certify those deliverables.

## Slide 6
2D / SYSTEM HARDENING DESIGN
Proposed boot trust and rollback architecture
MSU-2 · Task 2 evidence review · 17 Oct 2026 06
BOOT AUTHENTICATION
2d DESIGN CRITERION COMPLETE
Immutable key
Approved PPK hash
held by device
BootROM + FSBL
Authenticate first-stage
boot code
BOOT.BIN
Verify PMUFW, PL,
ATF and U-Boot
Signed FIT
Verify kernel, DTB
and root filesystem
Read-only OS
Run only the
authenticated release
UPDATE TRANSACTION AND AUTOMATIC ROLLBACK
Stage inactive slot
Keep confirmed
slot untouched
Verify release
Check signature,
digest and image
Trial boot
Bounded attempt
count and logs
Health check
Linux start + SPI
loopback smoke test
Confirm / rollback
Mark good or return
to prior slot
Design only: no signed boot image or A/B update is deployed. Development boot-header authentication is not fielded eFUSE-rooted trust. No eFUSE was programmed.
Notes: Design source: results/SOW_2D_SYSTEM_HARDENING_DESIGN_20261014.md.
Existing U-Boot environment fallback evidence and limitations: results/SOW_2G_RECOVERY_20260909.md.
AMD Zynq UltraScale+ MPSoC Software Developer Guide, Boot Time Security: https://docs.amd.com/r/en-US/ug1137-zynq-ultrascale-mpsoc-swdev/Boot-Time-Security.
AMD Embedded Design Tutorial, Enabling Boot Header Authentication: https://docs.amd.com/r/en-US/ug1209-embedded-design-tutorial/Enabling-Boot-Header-Authentication. Boot-header authentication omits the eFUSE key-hash and revocation checks; it is a development mechanism, not the fielded trust anchor.

## Slide 7
2E / COMPARATIVE FRAMEWORK STATUS
Linux thread CPU share declines as payload grows
MSU-2 · Task 2 evidence review · 17 Oct 2026 07
Chart: Payload size
| 1 B | 8 B | 16 B | 64 B | 128 B | 256 B | 512 B | 1,024 B | 4,096 B | 16,384 B | 65,536 B
Linux benchmark thread | 67.876 | 68.199 | 66.691 | 46.809 | 38.577 | 32.88 | 18.051 | 10.002 | 3.577 | 1.912 | 1.474
11,000 paired transfers
Zero transfer errors and RX mismatches in both recorded runs.
Linux thread CPU share: 67.9% at 1 B → 1.5% at 64 KiB.
Fixed-ladder Linux thread share is separate from sustained results. Bare metal reports 100% busy-wait core occupancy, not a PMU reading. Task 2e still needs the reliable clock/payload stress test.
Notes: Source CSV: results/linux_axi_spi_bringup_20261013/task2e_framework_metrics_20261014.csv.
Derived from raw Linux CLOCK_THREAD_CPUTIME_ID and CLOCK_MONOTONIC_RAW loop totals in results/linux_axi_spi_bringup_20261013/linux_benchmark_20261014.log.
Framework status and scope: results/SOW_2E_BENCHMARK_FRAMEWORK_STATUS_20261014.md. The utilization percentage is per benchmark thread normalized to one CPU core, not total system CPU utilization.
Physical closure experiment and remaining metric definitions: results/SOW_2E_BENCHMARK_CLOSURE_EXPERIMENT_20261015.md.
Paired sustained observations and clock/CPU limitations: results/task2e_sustainable_runner_20261016/SOW_2E_PAIRED_SUSTAINED_RESULTS_20261017.md and clock_readback_20261017.md.

## Slide 8
2G / MINIMAL STACK AND ROBUST UPDATE
A/B update prototype preserves the confirmed slot
MSU-2 · Task 2 evidence review · 17 Oct 2026 08
Authenticate
RSA/SHA-256
signature
Write inactive
Chunked write
+ fsync
Readback check
Digest + signature
re-verified
Trial boot
Two bounded
attempts
Confirm / rollback
Health result selects
new or known-good
4 / 4 HOST FAULT-INJECTION TESTS PASSED
Confirmed slot A stayed selected after invalid signatures, interrupted writes, boot-limit expiry, and an explicit failed health check.
Prototype boundary: host files and JSON control state. No U-Boot, SD-card, signed target image, hardware trust anchor, or ZCU102 power-loss test.
Task 2g remains partial until target integration, boot authentication, and recovery fault tests pass.
Notes: Report: results/SOW_2G_AB_UPDATE_PROTOTYPE_20261014.md.
Prototype: linux/appliance/ab_update_prototype.py. Tests: tests/test_task2g_ab_update.py.
Existing on-target U-Boot environment fallback evidence: results/SOW_2G_RECOVERY_20260909.md; it is a single-copy CRC fallback, not image/rootfs update recovery.
All four host tests passed on 2026-10-14. The diagram depicts reference logic, not an installed or hardware-rooted boot chain.

## Slide 9
TOOLCHAIN / LICENSE DIAGNOSTIC
Enterprise license passes ZCU9EG synthesis
MSU-2 · Task 2 evidence review · 17 Oct 2026 09
Sandboxed check
FlexNet could not read the workstation network-interface ID. It reported the node-locked license as invalid; Vivado then surfaced the failed checkout as an expired Synthesis feature.
Normal host access
The permanent Enterprise license matched the active workstation NIC. FlexNet approved the node, and Vivado granted Synthesis for xczu9eg.
Fresh synthesis for xczu9eg-ffvb1156-2-e completed with 0 errors
This was a small license-check design, not the project build. Synthesis uses the selected FPGA part; it does not communicate with the physical ZCU102 board.
Notes: Diagnostic report: results/vivado_license_diagnostic_20261015/README.md.
Successful Vivado 2025.1 synthesis transcript: results/vivado_license_diagnostic_20261015/zcu9eg_license_synthesis.log.
AMD Vivado 2025.1 UG973, Supported Devices: https://docs.amd.com/r/2025.1-English/ug973-vivado-release-notes-install-license/Supported-Devices. The Enterprise edition supports all Zynq UltraScale+ MPSoC devices.

## Slide 10
2G / TARGET EXECUTION
ZCU102 Linux update-control demonstration
MSU-2 · Task 2 evidence review · 17 Oct 2026 10
TEST CASE
UNSAFE BASELINE
SIGNED A/B REFERENCE
Valid release
Accepted in place
Verified; staged to B
Tampered release
Accepted altered bytes
Rejected; A unchanged
Interrupted write
Active A partially overwritten
A retained; no trial published
Failed trial health
Bad image remains active
Pending cleared; A selected
All four checks passed on the ZCU102 AArch64 Linux system using its OpenSSL runtime and temporary /tmp slots. This did not test BootROM/U-Boot, persistent boot state, or physical power-loss recovery.
Notes: Target report: results/SOW_2G_ZCU102_HARDENING_DEMO_20261015.md.
Target source/build: linux/appliance/hardening_contrast_board.c and scripts/build_task2g_board_demo.py. The application ran on newQspi, Linux 6.12.10-xilinx, and verified its RSA/SHA-256 fixture through target libcrypto.so.3.
Target executable SHA-256: 0ca6af020d16ea8174ec3d2f7ff625b1dd727870b1f28753898f51a98646f8e8. Captured output: results/task2g_board_contrast_20261015/target_run.log.
All file slots were in /tmp and removed by the application. The baseline intentionally lacks signature verification and recovery. The health failure and interrupted write are injected software cases, not a physical reset or boot test.
Tests: tests/test_task2g_board_demo_host.py and tests/test_task2g_ab_update.py. Target execution proves the user-space demo on the board, not its BootROM/FSBL/TF-A/U-Boot chain.

## Slide 11
2G / SIGNED IMAGE VERIFICATION
PetaLinux FIT signature rejects tampering
MSU-2 · Task 2 evidence review · 17 Oct 2026 11
U-BOOT 2025.01-XILINX · PETALINUX 2025.2 · VALIDATED XSA + BITSTREAM MATCH
Kernel + DTB
+ initrd
PetaLinux FIT
RSA-2048
signature
sha256 · msu2-test
Required key
in U-Boot DTB
key-msu2-test
Verify before
load
fit_check_sign
SIGNED BUILD ✓
U-Boot fit_check_sign accepted the PetaLinux configuration; FIT SHA-256: ca498597…e37222.
KERNEL BYTE FLIPPED ✕
Signature/hash check failed with “Bad Data Hash” before kernel load. Zero altered payload was accepted.
FIT build and tamper test passed; exact validated XSA/bitstream matched. No ZCU102 boot, trusted BootROM key, A/B rollback, or power-loss test.
Notes: Report: results/SOW_2G_PETALINUX_FIT_20261015.md. Build configuration templates: linux/appliance/verified_update/petalinux/.
Raw evidence, signed FIT, control DTB, tampered FIT, logs, metadata, and SHA-256 manifest: results/task2g_petalinux_fit_20261015/. Reproduce validation with scripts/task2g_verify_petalinux_fit.py.
PetaLinux project XSA SHA-256 exactly matches the validated 2026-09-29 XSA (e8b4626edb5949bc8adb14ae259802cdd24b16ea3f02daf0dd8fdbeb1cc0e7d7); deployed bitstream SHA-256 also matches (90f93479dd47c505b8f9e4fe6f4f18e853f8923d081f4b2037401ed3cb46994a). FIT DTB hash matches the regenerated system DTB.
U-Boot compiled and deployed. PetaLinux wrapper returned nonzero due unrelated exit-139 package tasks; relevant U-Boot, FIT, device-tree, and bitstream outputs were present and individually verified.
Signing key is disposable and remains outside the repository under the local PetaLinux build tree; it is not a production key. The valid image build is host-side evidence only and was not flashed to the target.
The embedded key node is required; signature algorithm is sha256,rsa2048. On payload modification, fit_check_sign reported “Bad hash value” and “Bad Data Hash”.
This is not hardware-rooted secure boot: BootROM/FSBL/TF-A/U-Boot authentication, protected key provisioning, persistent A/B slots and bootcount, Linux health confirmation, and target interruption testing remain open.

## Slide 12
2G / BOOT-CHAIN AUDIT
Generated boot policy can bypass FIT verification
MSU-2 · Task 2 evidence review · 17 Oct 2026 12
LIVE ZCU102 / newQspi
ACTIVE U-BOOT AND SD
Linux 6.12.10-xilinx
PetaLinux 2025.1 · root=/dev/ram0
SD image.ub (446dd475…) fails required-key verification: no signature node. boot.scr (6c555e63…) matches audited raw-boot fallback.
FPGA manager: operating. Loaded bitstream hash c27bb684… matches the validated Sep 29 .bit.bin.
bootcmd = run distro_bootcmd
boot_targets = mmc0, JTAG, QSPI, NAND, USB, SCSI, PXE, DHCP
bootdelay = 5 s. No bootlimit or upgrade_available. One SD partition; Linux root is RAM.
Host-built signed PetaLinux 2025.2 FIT is not installed or booted.
Conclusion: the SPI bitstream is validated, but the live board still runs an unsigned FIT through generic fail-open boot policy. Task 2g remains open until a trusted FIT-only chain and A/B recovery are tested.
Notes: Live target audit report and raw serial capture: results/task2g_live_board_audit_20261015/README.md and serial_session.log. Generated boot-script audit: results/task2g_bootflow_audit_20261015/.
Live SD boot.scr SHA-256 6c555e630e15ae1c7446f606cb99cfe5c52a0fde4e9deb2fa4e418c5d598b608 matches the captured generated script. The live image.ub SHA-256 is 446dd4756b4be2c29d513594e42adf45f0c90a362d2714dcc56f9ddbd5292bf0; required-key fit_check_sign failed because it has no signature subnode.
The kernel log reports firmware msu2_ratio2_j55_c27bb684.bit.bin loaded; its SHA-256 is c27bb684ca843e173585aed50096f95692530444b808ec948006dbb0d67f56fd, matching the validated Sep 29 bit.bin artifact. The FPGA manager reports operating.
Read-only fw_printenv from the SD copy showed bootcmd=run distro_bootcmd, broad boot_targets (mmc0 jtag mmc0 mmc1 qspi0 nand0 usb0 usb1 scsi0 pxe dhcp), bootdelay=5, bootseq=0, and unset bootlimit/upgrade_available. Rootfs is ram0 and the SD card has only mmcblk0p1. fw_setenv is not present in the running rootfs.
The signed FIT built with PetaLinux 2025.2 remains host-side and was not installed or booted. The boot-chain is not trusted until the running U-Boot and earlier BootROM/FSBL chain authenticate policy and image. No board media, FPGA, or persistent environment was modified; only temporary fw_env config/symlinks were created under /tmp.

## Slide 13
2A / 2E / ZCU102 J55 LOOPBACK
Fixed-trial Linux and bare-metal comparison
MSU-2 · Task 2 evidence review · 17 Oct 2026 13
Chart: Payload size
| 1 B | 8 B | 16 B | 64 B | 128 B | 256 B | 512 B | 1,024 B | 4,096 B | 16,384 B | 65,536 B
Linux (latency-derived rate) | 0.039606 | 0.2658 | 0.47759 | 0.99014 | 1.1965 | 1.3373 | 1.4113 | 1.4516 | 1.4848 | 1.4937 | 1.4961
Bare metal (latency-derived rate) | 0.14385 | 0.47227 | 0.56473 | 0.6599 | 0.679 | 0.68899 | 0.87146 | 1.0078 | 1.142 | 1.1813 | 1.1916
Linux: 11,000 / 11,000 pass
Bare metal: 11,000 / 11,000 pass. Both used 11 payloads × 1,000 trials.
Zero data errors. Linux was slower at 1–16 B, but had 20.4% lower latency at 64 KiB.
Same bitstream and 99.99 MHz PL0. Rates are derived from mean latency, not wire throughput. Linux uses CLOCK_MONOTONIC_RAW; bare metal uses XTime. Clock/CPU evidence supports a bounded comparison, not kernel-only attribution.
Task 2e remains open until the reliable clock/payload stress test is complete.
Notes: Revalidation report: results/linux_axi_spi_revalidation_20261016/README.md. Fixed-trial Linux log and rows are in that directory; the paired CSV is linux_vs_baremetal_fixed_trial_20261016.csv.
Bare-metal raw capture and metrics: results/task2e_sustainable_runner_20261016/baremetal_reboot_capture_20261016.raw.log and baremetal_reboot_metrics_20261016.csv. Both paths completed 11 sizes × 1,000 transfers with zero reported errors or receive mismatches.
The September 29 FPGA image hash was verified from the target SD source and staged Linux firmware file. FPGA Manager reported operating; it does not expose a bitstream readback hash. Linux clock framework showed IOPLL 1.49985 GHz and PL0 99.990 MHz. The 49.995 MHz SPI speed is the Linux requested/readback value; J55 SCK was measured at about 51 MHz previously for this exact image/configuration, but was not remeasured here.
The Linux benchmark uses CLOCK_MONOTONIC_RAW; bare metal uses XTime_GetTime. Post-run clock-register readback supports a derived 1.19988 GHz A53 full-rate clock and 99.990 MHz PL0. Effective payload rate is payload bytes divided by measured mean latency and is not physical wire throughput. The comparison is a same-workload board result, not causal attribution of kernel overhead.
Fixed-trial comparison report: results/linux_axi_spi_revalidation_20261016/README.md. Sustained Linux and bare-metal rates are presented on slide 14 and in results/task2e_sustainable_runner_20261016/SOW_2E_PAIRED_SUSTAINED_RESULTS_20261017.md. Physical J55 SCK about 51 MHz was measured previously for the same bitstream/configuration, not during sustained windows. Task 2e remains partial until the reliable clock/payload stress test is complete; backend ordering was not alternated and per-window clock sampling was not performed.

## Slide 14
2E / PAIRED 60-SECOND SPI WINDOWS
Sustained application throughput by payload
MSU-2 · Task 2 evidence review · 17 Oct 2026 14
Chart: Payload size
| 1 B | 8 B | 16 B | 64 B | 128 B | 256 B | 512 B | 1,024 B | 4,096 B | 16,384 B | 65,536 B
Linux median | 0.057753 | 0.26641 | 0.47259 | 0.98231 | 1.1919 | 1.3332 | 1.408 | 1.4492 | 1.4831 | 1.4924 | 1.4949
Bare-metal median | 0.14183 | 0.46772 | 0.56065 | 0.65589 | 0.675 | 0.68494 | 0.86513 | 0.99946 | 1.1312 | 1.1698 | 1.1797
66 / 66 points passed
Each backend ran 11 sizes × 3 × 60 seconds. All transfers were byte-verified; zero API errors and mismatches.
Crossover: bare metal leads at 1–16 B; Linux leads from 64 B upward.
Observed at this configuration: Linux 1.495 MB/s and bare metal 1.180 MB/s at 64 KiB. These are application rates, not wire limits. Clock readbacks support 1.2 GHz A53 / 99.99 MHz PL0; prior matching-setup J55 SCK was ~51 MHz.
Paired benchmark complete; Task 2e still needs the reliable clock/payload stress test.
Notes: Run report and interpretation: results/task2e_sustainable_runner_20261016/SOW_2E_PAIRED_SUSTAINED_RESULTS_20261017.md.
Editable chart source data: results/task2e_sustainable_runner_20261016/linux_baremetal_sustained_comparison_20261016.csv. Per-run raw-derived records: baremetal_sustained_runs_20261016.csv and linux_sustained_runs.csv.
Linux uses CLOCK_MONOTONIC_RAW; bare metal uses XTime_GetTime. Bare-metal occupancy is a busy-wait execution-model figure, not a PMU measure. Physical SCK (~51 MHz) was previously measured at J55 for the same bitstream/configuration but not remeasured during these windows. Clock readback detail: results/task2e_sustainable_runner_20261016/clock_readback_20261017.md. Linux ran before bare metal; order effects were not controlled.